## Slide 1: COMPUTER NETWORKING
LAB 4

## Slide 2: Dynamic Routing
OSPf single-area configuration

## Slide 3: OBJECTIVES
Configuration of the Router-ID for OSPF.
Establish OSPF on a specified interface or network. View OSPF operations using display commands. Advertisement of default routes in OSPF.
Change of the OSPF hello interval and dead interval. Familiarization with DR or BDR election on multi-access networks. Change of the OSPF route priority to manipulate DR election.

## Slide 4
Illustration of Routing Protocols
in Computer Network
Sources: https://www.geeksforgeeks.org

## Slide 5
Dynamic routing
Dynamic routing is a networking technique that provides optimal data routing. Unlike static routing, dynamic routing enables routers to select paths according to real-time logical network layout changes.
Advantages over routing
No need to know the destination networks
Updates the topology changes dynamically
Administrative work is reduced
Used for large organizations
OSPF Areas
The Open Shortest Path First (OSPF) protocol is a link-state hierarchical routing protocol primarily used within larger autonomous system networks.
OSPF Rules Includes:
Must have one area called as area 0
All areas must connect to area 0

## Slide 6
Topology

## Slide 7
Establish the basic system configuration and addressing for the lab
Prepare the environment

## Slide 8
Assign the value 10.0.1.1 (as used on logical interface loopback 0 for simplicity) as the router ID.
Use OSPF process 1 (the default process ), and specify network segments 10.0.1.0/24, 10.0.12.0/24, and 10.0.13.0/24 as part of OSPF area 0.
Manually assign the value 10.0.2.2 as the router ID. Use OSPF process 1 and advertise network segments 10.0.12.0/24 and 10.0.2.0/24 into OSPF area 0.
Configure OSPF

## Slide 9
After OSPF route convergence is complete, view routing tables of R1, R2 and R3.
Verify OSPF configuration

## Slide 10
Test connectivity
Use the ping command to test network connectivity between and R1 and between R2 and R3 at 10.0.3.3.

## Slide 11
Run the display ospf peer command to view the OSPF neighbor status.
The routing table does not contain the routes of the two networks.
The display ospf peer command displays detailed information about aany peering neighbors,
Test connectivity

## Slide 12
The display ospf peer brief command can also be used to display a condensed version of the OSPF peer information.
View Routing

## Slide 13: Thank you